Low Level Warning Panel

RCALM2

RCALM2L

RCALM2Q

RCALM2B

RCALM2LQ

RCALM2LB

RCALM2QB

RCALM2LQB

Installation and Operation Manual

Description Of Operation

The RCALM2 Display Panel provides a highly visible level warning display for water tanks.

The visual indication of power supply status (the green light) alerts the user in the event that power to the panel fails.

The amber low level light alerts the user to a low tank level and is accompanied by a repeating buzzer for audible alert.

Wiring to the amber light from a 2 way float switch can be reversed if desired to produce a high level warning function instead of low level.

Models

RCALM2

Light, Buzzer, BMS, 230vac Float Switch

RCALM2L

Light, Buzzer, BMS, 24vdc Float Switch

RCALM2Q

Light, BMS, 230vac Float Switch

RCALM2B

Light, Buzzer, 230vac Float Switch

RCALM2LQ

Light, BMS, 24vdc Float Switch

RCALM2LB

Light, Buzzer, 24vdc Float Switch

RCALM2QB

Light, 230vac Float Switch

RCALM2LQB

Light, 24vdc Float Switch

Installation

Safety Precautions

Mains Voltage – There are exposed electrical conductors inside this appliance. This appliance must be installed and serviced by a competent electrical technician to the current requirements of BS7671 and IEEE recommendations. Before servicing this appliance, normal safe isolation procedures should be implemented.

Do not touch any connection terminals while energised.

Do not attempt to service this item when wet, or in a wet or high humidity environment.

If the housing of the control panel becomes damaged, you must shut down and securely isolate this appliance immediately.

Included Components

RCALM2 Control Panel

Attached mains cable

Installation & Operation Manual

Float switch or level switch.

Layout

The control panel cannot be mounted outside, it is not fully weather resistant, but can be installed in sheltered outdoor locations (barns, covered areas, etc).

Suitable circuit protection must be installed and should include as a minimum a suitable earth, overcurrent protection, and residual current protection at 30mA, ideally on it's own circuit, but always in accordance with BS7671 and applicable regulations.

Control Panel Mounting

Open the cover of the control panel. There are 4 recesses, one on each corner of the panel. Drill through at these locations and attach to the wall or a suitable support, taking care not to damage cabling inside the panel. Fixings are not included and should be selected to suit the material to which the panel will be mounted.

Wiring

RCALM2/RCALM2Q

The control panel is supplied with wiring installed in the drawing shown above. The float or level switch needs to be fitted as shown in the next diagram.

Connections

Note that both wires to the float switch or level switch are live.

Note the green/yellow earth connection is provided for circuit protection to the appliance and has no function within the display panel which is Class 2 rated.

BMS Connection

RCALM2B/RCALM2QB

The control panel is supplied with wiring installed in the drawing shown above. The float or level switch needs to be fitted as shown in the next diagram.

Connections

Note that both wires to the float switch or level switch are live.

Note the green/yellow earth connection is provided for circuit protection to the appliance and has no function within the display panel which is Class 2 rated.

RCALM2L/RCALM2LQ

The control panel is supplied with wiring installed in the drawing shown above. The float or level switch needs to be fitted as shown in the next diagram.

Connections

Note that both wires to the float switch or level switch are live.

Note the green/yellow earth connection is provided for circuit protection to the appliance and has no function within the display panel which is Class 2 rated.

BMS WIRING

RCALM2LB/RCALM2LQB

The control panel is supplied with wiring installed in the drawing shown above. The float or level switch needs to be fitted as shown in the next diagram.

Connections

Note that both wires to the float switch or level switch are live.

Note the green/yellow earth connection is provided for circuit protection to the appliance and has no function within the display panel which is Class 2 rated.

Operation

Safety Precautions

Mains Voltage – There are exposed electrical conductors inside this appliance. Before servicing this appliance, normal safe isolation procedures should be implemented.

Do not attempt to operate this item when wet, or in a wet or high humidity environment.

If the housing of the control panel or attached wiring becomes damaged, you must shut down and securely isolate this appliance immediately.

Usage

Once energised the display panel will show a green light. This light is constantly energised as long as there is power to the panel. It indicates that the tank level is being monitored, and that there has been no disconnection or trip of any circuit breaker.

If the green light goes out, check the circuit breaker at the consumer unit supplying this circuit. Reset if necessary. If the circuit trips again do not reset but instead have the system checked by an electrically qualified service agent or a qualified electrician.

The amber light shows that the tank is at a low level, as indicated by the installed position of the float switch or level switch.

Specifications

Dimensions			180mm x 110mm x 90mm

Enclosure Material		Polystyrene

Ingress Protection		IP66

Electrical Protection		Class 2

Voltage			230VAC  1~